## Slide 1: SAP SYSTEM

## Slide 2: Work Center in SAP

## Slide 3: First Step: Identifying Labor Cost/ Hour & Electricity Cost/ Hour
Work Center Name | O/P per Shift | Electricity Consumption (KWH) / Shift | Rate/ KWH | Labor Requirement in Nos | Permanent Employee in Nos | Activity Cost for Labor / Month | Activity Cost for permanent Employee / Month | Labor Rate/ Hour | Permanent Employee Rate / Hour | Total Manpower cost / Hour | Electricity Cost / Hour
Biscuit Line | 10.67 MT | 1739 KW | 5.44 | 143 | 21 | =143*5600 =800800 | =Gross salary of 21 permanent Employee =576434 | =800800/25/8 =4004.00 | =576434/25/8 =2882.17 | =4004+2882.17 =6886 | =1739*5.44/8 =1182
Table: A sample Calculation for identifying Labor Cost & Electricity Cost.

## Slide 4: Second Step: KP26 Price Maintain in SAP
Hit KP26
Controlling Area: 1000

## Slide 5: Second Step: KP26 Price Maintain for Electricity Cost in SAP
Version: o
From Period: 1
To Period: 12
Fiscal Year: 2021 (Choice)
Cost Center: 1012000011 for Biscuit
Activity Type: 100211 for Electricity Cost
Click Overview
Change Fixed Price

## Slide 6: Second Step: KP26 Price Maintain for Labor Cost in SAP
Version: o
From Period: 1
To Period: 12
Fiscal Year: 2021 (Choice)
Cost Center: 1012000011 for Biscuit
Activity Type: 100211 for Labor Cost
Click Overview
Change Fixed Price

## Slide 7: Third Step: Work Center Creation
Work Center Creation : CRC1
Work Center Change : CRC2
Work Center Display : CRC3

## Slide 8: List of Work Centers for 1000 plant in SAP
Sl. No. | Plant | Work Center | Work Center Description | Cost Center | Activity Type For Machine | Activity Type For Labour
1 | 1000 | BAKERY | Bakery Production Line | 1013000011 | 100221 | 100222
2 | 1000 | BISCUIT | Biscuit Production Line | 1012000011 | 100211 | 100212
3 | 1000 | CAKELINE | Cake Production Line | 1014000011 | 100231 | 100232
4 | 1000 | CHANACHR | Chanachur Production Line | 1016000011 | 100251 | 100252
5 | 1000 | CHIPSLIN | Chips Production Line | 1015000011 | 100241 | 100242
6 | 1000 | FLRCRUSH | Flour Crushing Line | 1011000011 | 100201 | 100202
7 | 1000 | FLRPACKG | Flour Packaging Line | 1011000011 | 100203 | 100204
8 | 1000 | INSTNOOD | Insta Noodles Production Line | 1017000011 | 100261 | 100262
9 | 1000 | POWDRINK | Powderdrinks Production Line | 1018000011 | 100271 | 100272
10 | 1000 | PUFFRICE | Puffed Rice Production Line | 1027000011 | 100293 | 100294
11 | 1000 | SPECLPAK | Special Packaging Prod Line | 1021000007 | 100291 | 100292
12 | 1000 | STCKNOOD | Stick Noodles Production Line | 1017000011 | 100263 | 100264
13 | 1000 | WATERCAP | Water Cap Injection Line | 1019000011 | 100281 | 100282
14 | 1000 | WBLOWING | Water Blowing Prod Line | 1019000011 | 100285 | 100286
15 | 1000 | WFILLING | Water Filling Prod Line | 1019000011 | 100287 | 100288
16 | 1000 | WPREFORM | Water Preform Prod Line | 1019000011 | 100283 | 100284

## Slide 9: List of Work Centers for 2000 & 3000 plant in SAP
Sl. No. | Plant | Work Center | Work Center Description | Cost Center | Activity Type For Machine | Activity Type For Labour
1 | 2000 | SALTBULK | Salt Bulk Prod Line | 2011000011 | 200201 | 200202
2 | 2000 | SALTCP | SaltCP Prod Line | 2011000011 | 200203 | 200204
3 | 3000 | DISHWASH | IHCL DISH WASH WORK CENTER | 3015000011 | MACHIN | LABOUR
4 | 3000 | DMPLANT | DM Water Production Plant | 3022000011 | MACHIN | LABOUR
5 | 3000 | FLOORCLE | Floor Cleaner Production Line | 3013000011 | MACHIN | LABOUR
6 | 3000 | GLASSCLE | Glass Cleaner Production Line | 3016000011 | MACHIN | LABOUR
7 | 3000 | HANDWASH | Hand Wash Production Line | 3012000011 | MACHIN | LABOUR
8 | 3000 | MOTORWAS | Motor Wash Production Line | 3017000011 | MACHIN | LABOUR
9 | 3000 | MULTISUR | Multi Surface Cleaner Line | 3014000011 | MACHIN | LABOUR

## Slide 10: Work Center Creation (CRC1)
Hit CRC1
Plant: 100/200/300
Resource: Work Center Code (Suppose Spice for Spice Plant)
Resource Category: 008
Copy from:
If You want to create resource for 1000 plant then copy any resource of 1000 plant.

## Slide 11: Work Center Creation (CRC1) Cont…
Select
1. Basic Data
2. Default Values
3. Capacities
4. Scheduling
5. Costing
Then Click on Copy
In Basic Data Tab: Give Description of the work center.
Need not to change Default Value Tab, Capacities Tab & Scheduling Tab.

## Slide 12: Work Center Creation (CRC1) Cont…
Go to Costing Tab.
You will find Copy materials Cost center & Activity Type
Accounts department will give you cost center for that work center and you have to put it here.
Accounts department will give you activity type for labor and machine, you have to put it here.
After Completing costing Tab, Save the work center.

## Slide 13: ROUTING in SAP (C201)
Hit: C201

## Slide 14: ROUTING in SAP (C201) Cont…
Give: Material Code, Plant & Profile: PI01

## Slide 15: ROUTING in SAP (C201) Cont…
Give Status 4 & usage 1

## Slide 16: ROUTING in SAP (C201) Cont…
Select Sub Operation: 0010 Destination: 01
Give Work centre Code

## Slide 17: ROUTING in SAP (C201) Cont…
Give Base Quantity
Give Labor Hour and Machine Hour
Save

## Slide 18: Production Version in SAP (C223)
Hit: C223

## Slide 19: Production Version in SAP (C223) Cont….
Select Materail
Select New

## Slide 20: Production Version in SAP (C223) Cont….
Version No
Select BoM
Select Recipe
Select Group
Select Production Store Loc

## Slide 21: Production Version in SAP (C223) Cont….
Check
& save

## Slide 22: Production Version in SAP (C223) Cont….
After that Save the version

## Slide 23: ZPPBATCH
Enter New Material Group
Reference 1= 7 days Batch
Reference 2= 30 days Batch
Click on ZPPBATCH

## Slide 24: Quality Module

## Slide 25: QM Module Process Flow
RM
PM
FG Order Conformation
Result Recording & Usage Decision
QA32
Quality Inspection Report
ZQM_INSP
STOCK
MMBE (Individual)
MB52 (ALL)

## Slide 26: QM Module Master Data Maintain
Quality Parameter Creation (QS21)
Assign Quality Plan for RM, PM and FG. (QP01)
Release RM, PM & FG after completing quality Inspection. (QA32)
Quality Inspection Report
ZQM_INSP

## Slide 27: Quality Parameter Creation (QS21)
Two Types of Quality Parameter:
1. Quantitative
2. Qualitative

## Slide 28: Quality Parameter Creation (QS21) for Quantative
Hit QS21
Master Insp. Charac. : Name of the Parameter (Max length: 8 Character)

## Slide 29: Quality Parameter Creation (QS21) for Quantative cont….
Tick on Quantative
Select Incomplete copy Model
Status: Released
Short Text: Full name of parameter
Search Field: A portion of full name will used in searching the parameter.

## Slide 30: Quality Parameter Creation (QS21) for Quantative cont….
Check Tick on
Lower Specf. Limit
Upper Specf. Limit
Sampling Procedure
Sum Recording
Required Charc

## Slide 31: Quality Parameter Creation (QS21) for Quantative cont….
Check Tick on
Fixed Scope
No Documentation
Record Measured Vals
Print
No Formula

## Slide 32: Quality Parameter Creation (QS21) for Quantative cont….
After that Save the parameter and will shows created.

## Slide 33: Quality Parameter Creation (QS21) for Qualatative
Hit QS21
Master Insp. Charac. : Name of the Parameter (Max length: 8 Character)

## Slide 34: Quality Parameter Creation (QS21) for Qualatative Cont…
Status: Released
Short Text: Full name of parameter
Search Field: A portion of full name will used in searching the parameter.
Select complete copy Model
Tick on Qualatative

## Slide 35: Quality Parameter Creation (QS21) for Qualatative Cont…
Check Tick on
Char Attribute
Sampling Procedure
Sum Recording
Required Charc

## Slide 36: Quality Parameter Creation (QS21) for Qualatative Cont…
Check Tick on
Fixed Scope
No Documentation
Print

## Slide 37: Quality Parameter Creation (QS21) for Qualatative Cont…
This Attribute field will appear.

## Slide 38: Quality Parameter Creation (QS21) for Qualatative Cont…
Browse Quality Check Result

## Slide 39: Quality Parameter Creation (QS21) for Qualatative Cont…
Select Quality here

## Slide 40: Quality Parameter Creation (QS21) for Qualatative Cont…
Save it, Parameter will be created.

## Slide 41: Quality Plan Assignment (QP01)
Hit QP01

## Slide 42: Quality Plan Assignment (QP01) Cont…
Select Material
Select Plant & Enter

## Slide 43: Quality Plan Assignment (QP01) Cont…
Usage: Good Receipt
Overall Status: released General

## Slide 44: Quality Plan Assignment (QP01) Cont…
Go to Operations

## Slide 45: Quality Plan Assignment (QP01) Cont…
Select Work Centre & Control Key
Go to Inspection Characteristics

## Slide 46: Quality Plan Assignment (QP01) Cont…
Give Inspection Parameter & Give Value of Quantative Parameter
Then Save

## Slide 47: Result Recording & Usage Decision (QA32)

## Slide 48: Quality Result/ Decision (TCODE: QA32)
HIT QA32

## Slide 49: TCODE: QA32 Cont….
Click Execute
Material code is your choice
Giving Plant is mandatory
You can customize by selecting date

## Slide 50: TCODE: QA32 Cont….
Select the material
Click on result

## Slide 51: TCODE: QA32 Cont….
Click on Back

## Slide 52: TCODE: QA32 Cont….
Paramete
Specifications
Result

## Slide 53: TCODE: QA32 Cont….
Acceptable / Unacceptable (For Qualitative)

## Slide 54: TCODE: QA32 Cont….
Quantitative Value
Qualitative Value

## Slide 55: TCODE: QA32 Cont….
Usage Decision

## Slide 56: TCODE: QA32 Cont….
Click on UD Code (Accept/ Reject)

## Slide 57: TCODE: QA32 Cont….
Click on Inspection Lot Stock

## Slide 58: TCODE: QA32 Cont….
To Unrestricted Use= All Accepted

## Slide 59: TCODE: QA32 Cont….
Save it

## Slide 60: PP Module

## Slide 61: PP Module Process Flow
Planning Independent Requirement- PIR
MRP Running
MRP Result
Plan Order (FG & SFG)
Purchase Requisition (RM & PM)
RM
PM
FG
BOM
Order Release
Component List (ZPPSHOP)
Order Conformation (COR6N)
Report
(COOISPI)
Stock Transfer MIGO (311 Mov)
QC Checking QA32

## Slide 62: Master Data in PP
Material Master
BOM
Resource/ Work Center
Master Recipe
Production Version

## Slide 63: Bill of Material (BOM)
A bill of material is a complete, formally structured list of the components that make up a product or assembly.
The list contains a description and object number for each component, together with the quantity and unit of measure.

## Slide 64: Structure of BOM
FINISHED GOOD
RAW MATERIAL
PACKAGING
SEMI FINISHED GOODS
RAW MATERIAL
PACKAGING
(-) Bi-Product
(-) Bi-Product

## Slide 65: BOM in SAP (CS01)
Hit CS01

## Slide 66: CS01 Cont…..
Material Code
Plant:1000
Usage:1

## Slide 67: CS01 Cont….
Select L (Stock Item)
Select Material Code
Give Quantity

## Slide 68: CS01 Cont…..
Go to Header

## Slide 69: CS01 Cont….
Select Base Quantity

## Slide 70: CS01 Cont….
Select Item

## Slide 71: CS01 Cont…..
Go to Item

## Slide 72: CS01 Cont…..
Give Shop Floor Location
save

## Slide 73: Process Order Conformation (COR6N)

## Slide 74: Order Conformation (TCODE: COR6N)
COR6N

## Slide 75: TCODE: COR6N Cont….
Give Order Number then click enter

## Slide 76: TCODE: COR6N Cont….
Shows Order Qty (Put Here Actual Production quantity)

## Slide 77: TCODE: COR6N Cont….
Actual Production Qty
Click Here

## Slide 78: TCODE: COR6N Cont….
Now Click on goods movement

## Slide 79: TCODE: COR6N Cont….
Click Browse Icon Here then click enter

## Slide 80: TCODE: COR6N Cont….
Now gie the current date that will show black

## Slide 81: TCODE: COR6N Cont….
FG Batch number will show by clicking backspace in Keyboard and enter
RM Batch number will show like this way
PM Batch number shows blank means PM Batch is not required

## Slide 82: TCODE: COR6N Cont….
Save It

## Slide 83: TCODE: COR6N Cont….
After saving it will show the below message (Failed:0, means conformation ok)

## Slide 84: Material Requirement Document (TCODE: ZPPSHOP)
Enter ZPPSHOP

## Slide 85: TCODE: ZPPSHOP Contd…
Process Order Number
Plant : 1000 (IMPL)
2000 (ISCL)
3000 (IHCL)
Then Execute

## Slide 86: TCODE: ZPPSHOP Contd…
Click on Browse Icon

## Slide 87: TCODE: ZPPSHOP Contd…
Click on That

## Slide 88: TCODE: ZPPSHOP Contd…
Select ZLOC

## Slide 89: TCODE: ZPPSHOP Contd…
Click Print Preview

## Slide 90: TCODE: ZPPSHOP Contd…
Order Qty- A
Confirm
Qty-B
A - B
All Reservation-C
Qty in Shop-D
C-D
Issue Qty by store
Process order number
Order Quantity
Confirm quantity

## Slide 91: PR SYSTEM
Click on me51n
Click on object

## Slide 92: PR SYSTEM Cont….
For “A” = F/A
“requisition”=name
“val. Pri”=unit price
“short text”=material name with dept.
“qty,unit,delivery date,material grp”= 1010
“plant & store loc”=1000 & SPAR
“PGR”=130(service purchase)
Fill up the G/L Acc. & Order for each item
Save then collect the PR number

## Slide 93: Pending PR
Click on me5a
Pending PR

## Slide 94: THANK YOU ALL